EE 2201

Project #1 Solution

Problem 1 & Problem 2

clear all; close all;

T = input(' Sampling Period = ');

b=[T*T/(1+T+1.25*T*T)];

a=[1  -(2+T)/(1+T+1.25*T*T) 1/(1+T+1.25*T*T)];

%Form the D.T Difference Equation

Coefficients a & b

N = ceil(20/T);					%Compute the number of samples

n = 0:N;								%Form the Dicrete Time index n

t = n*T;								%Form the Continous Time index t

x=ones(1,length(n));				%Form the unit step input

y=filter(b,a,x); 					%Get the Output using the Matlab Function 
Filter

plot(t, y);							%Plot output

title('Step Response [y(t) vs t]');

ylabel('y(t)');

xlabel('t');

As the sampling parameter T decreases the output approaches the theoretically correct answer and hence T=0.01 gives the best results.

Problem 3

clear all; close all;

T=0.01;

b=[T*T/(1+T+1.25*T*T)];

a=[1  -(2+T)/(1+T+1.25*T*T) 1/(1+T+1.25*T*T)];

%Form the D.T Difference Equation 
Coefficients a & b

N = ceil(10/T);

n1= 1:N;

x1= ones(1,length(n1));					%Form a vector of all 1's

x2= zeros(1,length(n1));				%Form a vector of all 0's

x = [x1, x2];								%Form the input by joining x1 & x2

y = filter(b,a,x);					  	%Get the Output using the Matlab Function Filter

n = 1:2*N;									%Form the Discrete Time index n

t = n*T;										%Form the Continous Time index t

plot(t, y,'-',t,x,':');

legend('Output','Input');

title('Response to u(t) - u(t-10) [y(t) vs t]');

ylabel('y(t)');

xlabel('t');

Output1 is the response for the input x(t) = u(t)

Output2 is the response for the input x(t) = -u(t-10).

By the principle of Superposition the response to u(t) – u(t-10) should be Output1+Output2 which is justified by the above plot.

# Problem 4

## The required difference equation is

y[n]   –            	    y[n-1]		=                    T/RC x[n]

[1+ (1000+R)T/(1000RC)] 		[1+ (1000+R)T/(1000RC)]

# Problem 5 & 6

clear all; close all;

T = input(' Sampling Period = ');

R = input(' Resistance = ');

C = input(' Capacitance = ');

temp = (1+(1000+R)/(1000*R*C)*T);

b= 1/(R*C)*T/temp;

a = [ 1 -1/temp];								%Form the Discrete Time 
Difference Equation Coefficients

Tp = 1/60;										%Tp is the period of x(t)

N = ceil(10*Tp/T);							%Compute the number of samples

n = 1:N;											%Form the Discrete Time index n

v = 120*sqrt(2)*cos(120*pi*n*T);			%Form the input x(t)

x = abs(v);										%Get the input v(t) to RC filter

y=filter(b,a,x);					   		%Get the Output using the Matlab 
Function Filter

subplot(311), plot(n*T, v);

ylabel('v(t)');

subplot(312), plot(n*T,x);

ylabel('x(t)');

subplot(313), plot(n*T,y);

ylabel('y(t)');

xlabel('t');

According to the sampling theorem the minimum sampling frequency is equal to twice the maximum frequency of the input signal. Hence the maximum value of T that we could use to sample the input sinusoid is 1/120 seconds. T should be much smaller than this to get a good approximation of the input signal.

Problem 7

C should be increased to make the ripples smaller in the output. C = 0.00001 (10(F) is necessary to achieve less than 1 volt of peak-to-peak ripple about the constant output value. The DC output voltage of this power supply = 5 V.

Problem Optional

For DC output of 10V with less than 1V of peak-to-peak ripple,

R= 9800 ohms & C= 0.00002 (20(F)